## Slide 1
DX University
Visalia California – 2014

## Slide 2
Station & Antenna Considerations
Ned Sterns AA7A

## Slide 3: Ned Stearns AA7A
First licensed in 1963 at age 12, he has been a serious Dxer since 1974.
Top of the Honor Roll, 5BWAZ, Satellite DXCC, and the first ever 11-band DXCC (160 through 2 meters, inclusive).
Dxpeditions in 1979 as AA7A/VP2A ; 1999 as 3B9R ; 2000 as K5K.
Member of the VooDoo Contest Group since 2005. Currently the team co-leader and station designer.
Serves as a director on the NCDXF.

## Slide 4: Topics
Radios
Antennas
Other Station Elements
Station Layout

## Slide 5
Critical receiver requirement
  Selectivity
  Dynamic range
  Split frequency operation
Advanced capability
  Second receiver or sub-receiver
  Diversity reception
  Panadapter displays
  Software Defined Radios (SDR)
Radio Equipment - Receivers

## Slide 6
Roofing Filters
  Limits power applied to non-linear receiver elements
Digital Signal Processing
  Bandpass filters
  Notch filters
  Noise Reduction algorithms
  Noise Blanking
Receiver Selectivity

## Slide 7
Receiver Dynamic Range
One simple definition: Blocking Dynamic Range
    Copy a weak signal simultaneously with a high level, off-channel signal
    Ratio of signal amplitudes at point when degradation of weak signal starts
Radio | BDR, dB
Elecraft K3 | 139
Ten Tec Orion II | 136
Yaesu FTdx9000D | 127
ICOM IC-7800 | 115
ICOM IC-756PROIII | 101

## Slide 8
Power level
  Heat is at the root of most component failures
  Consider operating radios well below maximum power levels
Modulation Quality – How good (or wide) is your signal?
  Undesirable sidebands – clicks or ɸ noise will get you noticed
  Reduce audio distortion – audio processing may result in higher average power but can result in lower understandability
Consider covering all the operating modes
    Traditional modes (CW, SSB, AM, RTTY) are native
    New modes (e.g. PSK, JT65) may require external modems
Transmitter - Critical Requirements

## Slide 9
Requirements related to effective DXing
  Pattern matching propagation path to DX
  Pattern reducing effects of interference
  Efficiency
General characteristics
  Efficient antennas are likely to be narrowband
  Antennas are the best investment in your station
  Reliability can be more important than performance
  Higher antennas work DX better than lower ones
Antennas

## Slide 10
Transmit antennas
Verticals
Dipoles (as high as possible)
Low frequencies antennas (160 & 80 m)

## Slide 11
Receive antennas
Beverages
Loops
(ground-dependent antennas)
Flag/pennants
(ground-independent antennas)
4-square short verticals
Low frequencies antennas (160 & 80 m)

## Slide 12
Monoband antennas
  Full size: Yagi1
  Shortened: Moxon2
1
2
Antennas - HF

## Slide 13
Multi-band antennas (Fixed)
Hexbeam1
Spider beam2
Log periodic3
Quad4
Multiband Yagi5
1
2
4
3
5
Antennas - HF

## Slide 14
Adjustable
SteppIR
Antennas - HF

## Slide 15
Grounding
  Nearby lightning strike protection
  Shock hazard mitigation
  Audio ground loop reduction
Other Station Elements

## Slide 16
Filtering
  Harmonic suppression
  BCI reduction
  Protection of local equipment
Other Station Elements

## Slide 17
Audio Transducers
  Headphones / speakers
  Microphones
  PC CODECs
Other Station Elements

## Slide 18
Station Layout Considerations
Reduce stress and strain
  Organization of equipment
  Neck strain reduction
  Minimize eye strain
Lighting
  Must see the radio knobs
  Must see keyboards
Ambient sound
  Fan noise
  Clunking relays
Posterior comfort

## Slide 19
HF Radio #1
HF Radio #2
HF Amplifier #2
HF Amplifier #1
HF Amplifier #3
HF Logging Computer mon #1
HF SDR #3
SDR Display
Rotor Display
12-channel Audio Mixer
HF Logging Computer mon #2
HF Wattmeter
AA7A Station – 10 Feb 2012 (at 1646 Z )

## Slide 20
Primary Focus
Secondary Focus
Secondary Focus
AA7A Station – Operator Focus

## Slide 21
Happy Hunting!
Station & Antenna Considerations
Notes: LAST SLIDE IN PRESENTATION